## Slide 1: Retention time, iRT, and standards
Northeastern University
Targeted Proteomics with Skyline
Monday, May 1 - 1:30 pm session

## Slide 2: Objectives
Understand from an applications framework what retention time is
Compare how retention time is calculated without prior knowledge of peptide RT versus with prior knowledge
Establish comfortability with Skyline’s retention time calculator for scheduled methods

## Slide 3: Agenda
Overview of retention time
Predicting retention time with SSRCalc and iRT
Choosing RT standards
Hands on: building an iRT calculator
--break--
LC Optimization, part 1
  Hands on: Effect of LC gradient on quantitative MS
LC Optimization, part 2
  Hands on: Effect of scheduling on quantitative MS

## Slide 4: Review: Setting up a targeted MS method

## Slide 5: Can’t do “LC-MS” without the LC!
Liquid Chromatography (LC): Analytes dissolved in mobile phase move through the stationary phase at a speed that depends on the analyte (more details on analyte “speed” later)
Retention time (RT): timepoint in the LC gradient when a given peptide elutes

## Slide 6: Native visualization of multiple peptides in Skyline
Tip! Hold “ctrl” + select peptides to view their chromatogram

## Slide 7: Peptide retention times can be predicted using bioinformatic algorithms (SSRCalc)
Krokhin 2004
SSRCalc: Sequence-Specific Retention Calculator
sums retention coefficients of individual amino acids, plus additionally considers retention coefficients N-term amino acid

## Slide 8: Viewing SSRCalc results in Skyline
Tip! In the Retention Time pane, right click and select “Graph” > “Regression” > “Score To Run”

## Slide 9: Reading a regression-view Retention Time pane with an SSRCalc calculator
SSRCalc score
“real” RT
Each point is a peptide

## Slide 13
Outliers!

## Slide 14: Peptide RT can be empirically determined using standards (iRT)
iRT: a technique for storing calibrated, empirically measured peptide retention times in a library for future use in retention time prediction
Escher 2012

## Slide 15: Reading a regression-view Retention Time pane with an iRT calculator

## Slide 16: Regression-view Retention Time pane: SSRCalc and iRT calculator
iRT value
“real” RT
Each point is a peptide
SSRCalc score

## Slide 17: Empirically derived retention times (iRT) outperform computationally predicted RT (SSRCalc)
Escher 2012

## Slide 18: Peptide standards establish the correlation between RT prediction score and measured RT
Hands-on iRT calculators from Brendan after this!

## Slide 19: Many types of RT standards to choose from
Exogenous commercial standard spike-in
  Pro: reliability
  Con: price
  Ex: Pierce, Sigma Aldrich, Biognosys, …
Experiment-specific endogenous standards
  Pro: Cheap, simple implementation
  Con: Must see those peptides in every sample!
  Ex: Common contaminants (human keratin), abundant system-specific peptides (albumin)

## Slide 20: RT standards and prediction guard against RT drift
Tip! In the Retention Times pane, right click and select “Graph” > “Replicate Comparison” (you can click and drag areas to zoom, too)
Same column over time 
New column

## Slide 21: Conclusions
Peptide retention time is influenced by the LC, not by the MS
SSRCalc predicts retention time with no knowledge other than the peptide sequence
iRT uses peptide standards to build a normalized peptide RT that can then be applied to unknown peptides
Skyline supports both SSRCalc- and iRT-based retention time prediction

## Slide 22: For more information…
Literature
  iRT:
  http://onlinelibrary.wiley.com/doi/10.1002/pmic.201100463/abstract
  SSRCalc:
  http://www.mcponline.org/content/3/9/908.full.pdf
Skyline iRT calculator tutorials
  http://dia-swath-course.ethz.ch/tutorials2015/Tutorial-5_Scheduling.pdf
  https://skyline.ms/wiki/home/software/Skyline/page.view?name=tutorial_irt
Retention time in Skyline (pp 7-12)
  https://skyline.ms/_webdav/home/software/Skyline/%40files/tutorials/MethodRefine-1_4.pdf

## Slide 23: Hands on: Building an iRT calculator
Take home:
  Create and apply an iRT calculator within a Skyline document
  Interpret regression visualizations of RT