## Slide 1: LC optimization
Northeastern University
Targeted Proteomics with Skyline
Monday, May 1 - 3:30 pm session

## Slide 2: Objectives
Explore how to manipulate liquid chromatography to achieve your experimental goals
Build intuition for the effects of liquid chromatography on quantitative MS data

## Slide 3: Agenda
Overview of retention time
Predicting retention time with SSRCalc and iRT
Choosing RT standards
Hands on: building a retention time calculator
--break--
LC Optimization, part 1
  Hands on: Effect of LC gradient on quantitative MS
LC Optimization, part 2
  Hands on: Effect of scheduling on quantitative MS

## Slide 4: Peak picking with retention time information
Prediction of m/z good, prediction of RT not so good
Knowledge of when a peptide elutes helps the software “pick” the right peptide peak
Recall: empirically sourced RT is more accurate than predicted!

## Slide 5: Chromatography has quantitative consequences

## Slide 6: Chromatography has quantitative consequences

## Slide 7: Chromatography has quantitative consequences
cycle time

## Slide 8: Quantitative accuracy is a function of dwell time and cycle time
Lange 2008

## Slide 9: Balancing number of targets, dwell time, and acquisition time
Target list
Dwell time
Acquisition time

## Slide 10: Balancing number of targets, dwell time, and acquisition time
Target list
Dwell time
Acquisition time
Number of precursors/transitions
Total duration of the acquisition
Amount of time spent on each scan

## Slide 11: Balancing number of targets, dwell time, and acquisition time
Target list
Dwell time
Acquisition time
# Targets * dwell time = cycle time

## Slide 12: Points-across-peak can be manipulated by number of scans or by peak width
cycle time

## Slide 13: Peak width is determined by a combination of column and gradient details
Important Column Details
Length (aka bed volume)
Stationary phase (packing material)
Inner diameter (ID)

## Slide 14
Faster separation
Greater loading capacity
Greater sensitivity

## Slide 15: Gradient details – the separation aka analytical gradient – also affect separation
Important Gradient Details
Starting condition
Duration of separation
Start/end %B
Equally important is the “wash” and “reequilibration” step, but for now we’ll focus on just separation/analytical

## Slide 16: Analytical component is specified by the duration of separation, and the starting %B and ending %B
Chart: Time (min)
| 0 | 1 | 18 | 19 | 23 | 24 | 34
grad01 | 0 | 8 | 35 | 95 | 95 | 50 | 50
Separating aka analytical
(when peptides elute)
Wash
(“clean” column)
Reequilibration
(prepare column to bind next sample’s peptides)
Hands on coming up

## Slide 17: Conclusions
Column details:
  Bed volume
  packing material
  Tubing ID
Gradient details:
  Starting condition
  Duration of separation
  Start/end %B
Components to an LC method

## Slide 18: Hands on: gradient effects on method
Take home:
  Build intuition for how separation affects data
  Practice utilization of Skyline Document Grid (points across peak)

## Slide 19: Agenda
Overview of retention time
Predicting retention time with SSRCalc and iRT
Choosing RT standards
Hands on: building a retention time calculator
--break--
LC Optimization, part 1
  Hands on: Effect of LC gradient on quantitative MS
LC Optimization, part 2
  Hands on: Effect of scheduling on quantitative MS

## Slide 20: Hands on: gradients differed in separation, but same wash and reequilibration
Chart: Time (min)
| 0 | 1 | 18 | 19 | 23 | 24 | 34
grad01 | 0 | 8 | 35 | 95 | 95 | 50 | 50
grad02 | 0 | 10 | 43.75 | 95 | 95 | 50 | 50
grad03 | 0 | 12 | 52.5 | 95 | 95 | 50 | 50
grad04 | 0 | 16 | 70 | 95 | 95 | 50 | 50
grad05 | 0 | 6 | 26.25 | 95 | 95 | 50 | 50
grad06 | 0 | 8.8 | 38.5 | 95 | 95 | 50 | 50
grad07 | 0 | 7.2 | 31.5 | 95 | 95 | 50 | 50

## Slide 21: Separation gradients aren’t required to have one constant slope
Chart: % B
| 0 | 2 | 8 | 12 | 14 | 15 | 18 | 18.100000000000001 | 25 | 25.1
grad 01 | 0 | 9 | 15 | 25 | 50 | 95 | 95 | 50 | 50 | 50
Multi step separation
Quick bump to 5-10%
Long and shallow during “typical” peptide elution
Sharp bump to elute hydrophobics

## Slide 22: Gradient wash and reequilibration rule-of-thumbs
Column bed volume: V = π * r * 2h
Typically you know the inner diameter (ID) of the column (r) and the length of your column (h)
Step | Solvent | Volume
Separation | Range (2-60% B) | --
Wash | 70-98% B | 1x column volume
Reequilibration | Starting conditions (2-5% B) | 2-3x column volume
Notes: 100 um ID = 0.1 mm diameter = 0.05 mm radius ; 25 cm column = 250 mm height ;

## Slide 23: Reequilibration practice example
Column bed volume: V = π * r * 2h
Reequilibrate with 2-3x column volume
Given:
100 um ID
25 cm bed length
Notes: 100 um ID = 0.1 mm diameter = 0.05 mm radius ; 25 cm column = 250 mm height ;

## Slide 24: Reequilibration practice example
Column bed volume: V = π * r * 2h
Reequilibrate with 2-3x column volume
Bed volume:
1.96 ul
Bed volume (1.96 ul) * 2 = 4 ul
Bed volume (1.96 ul) * 3 = 6 ul
4 – 6 ul
Reequilibration volume (4 ul) / Flow rate (0.2 ul/min) = 20 min
Reequilibration volume (6 ul) / Flow rate (0.2 ul/min) = 30 min
20 – 30 min
Given:
100 um ID
25 cm bed length
Wash for 10 min
Tip: Increasing flow rate can help reequilibrate faster, but be cautious of back pressure
Notes: 100 um ID = 0.1 mm diameter = 0.05 mm radius ; 25 cm column = 250 mm height
Flow rate of 0.3 ul/min = 12 – 20 min!

## Slide 25: Tips and tricks 1
Increasing flow rate can help reequilibrate faster, but be cautious of back pressure
  Shorter columns generate less backpressure (can flow faster)
  Bigger beads generate less backpressure
  Heating increases the maximum flow rate your column can handle

## Slide 26: Tips and tricks 2
“Dead volume” means you have to keep pumping solvent to “see” your peptides elute
  don’t just stop the method at your peptide’s elution percentage
  “dead volume” can be calculated, but it’s easier to simply observe
University of Washington Proteomics Resource (UWPR)

## Slide 27: Tips and tricks 3
Use of a “trap” aka “precolumn” is helpful in certain experiments
  What it is: a short (2-3cm) column placed between the HPLC gradient delivery and the micro-tee
  What it does: concentrates the sample bolus, washes salts from sample
  What you gain: trap gets “dirty” before your analytical column does, and changing a dirty trap is less disruptive to chromatographic conditions than changing the analytical column

## Slide 28: “Scheduling” targeted methods makes efficient use of MS/MS scans
Cycle time
MS/MS scan
Point on peak
Targeted acquisition of “red” m/z

## Slide 29: “Scheduling” targeted methods makes efficient use of MS/MS scans
Unscheduled
Scheduled

## Slide 30: Comparison of unscheduled vs scheduled
 | Unscheduled |  | Scheduled
Workflow | “Set it and forget it” |  | Requires periodic adjustment to account for peptide RT drift
Target list | Less targets (limited by minimum 3-5 points across the peak) |  | More targets
Quantitative quality | Less points-across-peak on average (fixed cycle time across gradient) |  | More points-across-the-peak on average (variable cycle times across gradient)

## Slide 31: Recall: balancing number of targets with acquisition time and dwell time

## Slide 32: When scheduling isn’t enough, multiple injections is a possibility

## Slide 33: Multiple injections splits method into parts
Injection #1: blue and red
Injection #2: green

## Slide 34: Process and visualize multiple injection experiments as single files using Skyline
Tip! Import multiple injections as a single run:
File >
Import >
Results >
Add multi-injection
Add new replicate + Add files to an existing replicate

## Slide 35: Conclusions
Various “tricks” help meet experimental needs
  Chromatography: flow rates, heat, trapping, …
  MS: scheduling, multi-injection, …
Step | Solvent | Volume
Separation | Range (2-60% B) | --
Wash | 70-98% B | 1x column volume
Reequilibration | Starting conditions (2-5% B) | 2-3x column volume

## Slide 36: For more information…
Solid HPLC Resource
  http://www.ionsource.com/tutorial/chromatography/rphplc.htm
Full Skyline method refinement tutorial:
  https://skyline.ms/labkey/_webdav/home/software/Skyline/%40files/tutorials/MethodRefine-1_4.pdf
Unmentioned tip: Ion pairing additives (like DMSO)
  http://www.nature.com/nmeth/journal/v10/n10/abs/nmeth.2610.html

## Slide 37: Hands on: Scheduled vs unscheduled
Take home:
  Differentiate data analysis between scheduled vs unscheduled
  Explore how peak picking is affected by scheduling
  Locate and manipulate the scheduling window visualization in Skyline